## Slide 1: Anacostia River 2018 Tributary Background Study

## Slide 2: Purpose of the NPS Anacostia River Tributary Sediment Sampling
Provide data to determine concentrations of COCs in bottom sediment located upstream of the tidal Anacostia River to assist in determination of anthropogenic background concentrations.
Provide evidence of possible point sources of COCs located upstream of ARSP area.
To address comments received on RI regarding use of Potomac River Reference Area to determine background concentrations of COCs.
EPA Definition of Anthropogenic Background – “Human-made substances present in the environment as a result of human activities (not specifically related to the CERCLA release in question)” (Role of Background in the CERCLA Cleanup Program April 26, 2002)
2

## Slide 3: USGS Tributary Study
Work Completed by USGS in 2017 indicated the following five tributaries are responsible for majority of flow into tidal Anacostia River:
Northwest Branch
  Northeast Branch
  Lower Beaverdam Creek
  Watts Branch
  Hickey Run
Lower Beaverdam Creek found to contain highest level of PCBs in suspended sediments.
3
Notes: Informed scope of NPS Trib Study

## Slide 4
Potomac Reference Area
Tidal Anacostia River
4

## Slide 5: NPS Background Tributary Study
Collected bottom sediment samples (top 6 inches of sediment) from the five major tributaries
Comparable to surface sediment samples collected during RI in Anacostia and Potomac Reference Area
  Analyzed for following COCs:
    PCB Congeners
    Dioxins and Furans
    Parent and alkylated PAHs
    Pesticides
    Mercury
    Also analyzed for TOC and grain size
5
Notes: Risk assessment based on fish exposure to top 6 inches of sediment.
Fine grained material for comparability with Anacostia River sediment

## Slide 6: NPS Background Tributary Study
Total of 64 samples collected from 55 locations week of November 26th
Sample collection biased for fine grained material

## Slide 9: Statistical Analysis of Data
Compare sample results within each tributary to consider influence from suspected point sources.
Filter data set to remove obvious point source bias/influence for each COC.
Compare tributary data to Anacostia River and Potomac River reference area data to potentially refine anthropogenic background concentrations.
9

## Slide 10: Schedule
Unvalidated laboratory data due December 2018
Validated data due early March 2019
  NPS will prepare report summarizing sampling results and will work with DOEE to incorporate results into RI and FS as appropriate
  Draft report completed May 2019
10